## Slide 1: COMP90007 Internet Technologies Lab – Network Analysis
Week 4

## Slide 2
Slides
If there is any error in slides, please point it out.
Please refer to solution on LMS for standard answers
https://github.com/SiaHuo/COMP90007Workshops

## Slide 3
Go to LMS – Assignment - Network Analysis Assignment
It is recommended that you perform these tasks in a consistent networking environment to reduce the variance in your results

## Slide 4
Go to LMS – Assignment - Network Analysis Assignment
It is recommended that you perform these tasks in a consistent networking environment to reduce the variance in your results

## Slide 5
Experiment 1 -- Measuring the hop count
traceroute/tracert(packet)
Represent the hop number from the source to the target
Mac User: Open Terminal
traceroute –nw 1 cis.unimelb.edu.au
Windows User: Open Command Prompt
tracert cis.unimelb.edu.au
Computer network diagnostic tool for displaying the route and measuring transit delays of packets across an Internet Protocol (IP)

## Slide 6
Mac User: Open Terminal
traceroute –nw 1 cis.unimelb.edu.au
Windows User: Open Command Prompt
tracert cis.unimelb.edu.au
**** time out hops still count
traceoute –P icmp cis.unimelb.edu.au

## Slide 7
**** time out hops still count
traceoute –P icmp cis.unimelb.edu.au
Mac User: Open Terminal
traceroute –nw 1 cis.unimelb.edu.au
Windows User: Open Command Prompt
tracert cis.unimelb.edu.au

## Slide 8
Parameters
Mac User: man traceroute
Windows User: tracert /?

## Slide 9
Task 1
Plot the hop count versus the approximate geographical distance from Melbourne. Do you observe a correlation? Why? Why not?

## Slide 10
Task 1
Plot the hop count versus the approximate geographical distance from Melbourne. Do you observe a correlation? Why? Why not?
Scatter plot

## Slide 11
Experiment 2 Measuring delay and jitter
ping
Windows User: ping cis.unimelb.edu.au
Mac User: ping –c 5 cis.unimelb.edu.au

## Slide 12
Windows User: ping cis.unimelb.edu.au
Mac User: ping –c 5 cis.unimelb.edu.au
Round-trip time (RTT): is the length of time it takes for a single to be sent plus the length of time it takes for an acknowledgement of that signal to be received.

## Slide 13
How to calculate jitter?
The standard deviation of the round-trip delay time will be taken as the value for jitter for this project
Jitter

## Slide 14
Task 2
Run the ping command 3 times of each host, and find the average round-trip delay and jitter by calculating the standard deviation, for each host in Table1

## Slide 15
Experiment 3 Bandwidth
iperf
Download to your own laptop
Use university servers: digitalis, digitalis2
Server mode –s / Client mode –c
Server mode: iperf3 –s
Client mode: iperf3 -c iperf.eenet.ee
An iperf instance running in client mode will connect to the server, and packets will be exchanged and timed between the two hosts to calculate the bandwidth

## Slide 16
iperf3 –c bouygues.iperf.fr

## Slide 17
How to access to unimelb server: deigitalis, digitalis2
(refer to the document on LMS)
Mac user: ssh username@digitalis2.eng.unimelb.edu.au
Windows user: PuTTy
Download a software called PuTTY, http://www.putty.org/

## Slide 19
VPN

## Slide 20
Tips：
server

## Slide 21
Tips：
Appendix

## Slide 22
Tips：
Consistency
You should test all 8 servers either on ur own laptop, or digitalis, or VM.
Do not mix.
It is recommended that you perform these tasks in a consistent networking environment to reduce the variance in your results

## Slide 23
Tips：
Order
traceroute --- hop number
ping --- delay and jitter
iperf --- bandwidth